## Slide 1: Best Practice for Using HDP with HNAS

## Slide 2
Before we dive deeper into the best practices of using HDP with HNAS, it is important for us to better understand the HNAS storage concepts

## Slide 3: LUN PROVISIONING SYSTEM DRIVE GROUPS
System Drive Groups (SDG) serve two important functions within HNAS
Help HNAS understand relationship between RGs and SDs
  Typically 1 LUN per RG, mandates 1 SD per SDG
  Multi LUN RG, will map multiple SDs to an SDG
  HNAS v11.2 provides auto-grouping of LUNs from Hitachi Storage
Intelligent Write Cursor
  Each File System has a main cursor that tracks which SDG it is currently using
  Each SDG has its own write cursor that it uses to track which 4MB stripe it is currently pointing to
  Each 4MB stripe in each SDG is written to in turn as the main file system write cursor moves from SDG to SDG within a stripe set
SD
SD
SD
SD
SD
RG
RG
RG
RG
RG
SD
SD
SD
SD
SD
LUN
LUN
LUN
LUN
LUN
SDG
SDG
SDG
SDG
SDG

## Slide 4: RG and LUN BEST PRACTICES For NON HDP scenarios
  HNAS writes to all SDs within a stripeset in parallel so 1 LUN per RG avoids disk contention
  The exception is SSD/HAF where up to 8 SD per RG is recommended (provides more Q Depth)
  Enterprise Platform max LUN size is 2.9TB
      Either create multiple LDEVs per RG using SDGs as appropriate or use HDP (which allows larger LUN sizes)
RAID5 4+1 typically works very well with HNAS with 4 SDs = 20 drives, so incremental expansion of the Span is 20 drives
  If using 8+1 then 4 SDs = 36 drives, so incremental expansion requires almost twice as many drives
  (See section on span expansion for more details)
Balance that incremental expansion against scalability requirements
  If using 4+1 with 600GB, then 512SD will scale only to 1.2PB
  Churn typically will result in FS fragmentation over time, which leads to reduced Superflush – less sequential writes, more random writes
  RAID10 masks the impact of random writes
  RAID6 is the lowest performing configuration when random writes take hold
When using native RGs
then create 1 LUN per RG
and
1 SDG per SD
600GB drives (more risk with 900GB drives), but RAID6 recommended with larger drives and large pools.
RAID10 2+2 works best in
file systems/workloads
that
experience significant “churn”

## Slide 5: Storage POOLS and STRIPESETS
LU
LU
LU
LU
SD
SD
SD
SD
Chunks
STRIPESET
HNAS Storage Pool/Span consists of one or more System Drives (SD)
  The term “Span” and “Storage Pool” are interchangeable.
HNAS creates an SD for each LUN that is discovered. System Drives must be allowed access before HNAS can utilize them.
When you initially create a span, the server creates a single stripeset using the specified SDs
This means that a large sequential I/O to one of the span's file systems will use several SDs to increases performance
Span capacity is broken down into chunks. File systems on the span are allocated chunks from this storage pool
A Span can be expanded but cannot be shrunk
4MiB
STRIPELINE
STORAGE POOL
Notes: HNAS uses 4MiB stripes -- it looks (and potentially writes to) 4MiB of space on one LU (SD) before moving on to the next.
So the stripeline size on any one stripeset is 4MiB multiplied by the number of LUs in the stripeset – in the diagram above 16MiB
A chunk resides entirely on one stripeset and contains a whole number of stripelines. It therefore draws exactly the same amount of space from all the LUs in the stripeset. This -- the fact that one stripeset may have seven LUs, and therefore a 28MiB stripeline size, and the next stripeset may have nine LUS, and therefore a 36MiB stripeline size -- is one reason why a span's chunks aren't all the same size, and why none of them may exactly equal the guideline chunk size.set.

## Slide 6: STORAGE POOL BEST PRACTICES STRIPESIZE
A stripeset must contain at least 2 SDs, but a stripeset should be configured with a minimum of 4 SDs to provide sufficient Q-Depth to service I/O requests. More SDs per Stripeset provides more write queues for that stripeset.
One should balance # of SDs per stripeset against performance and incremental expansion requirements
  If a customer knows a pool will never be expanded, one could place all SDs in a single stripeset
  If a customer has minimal performance requirements but desires very granular expansion then perhaps 2 SDs per Stripe set will work for them … As with all things ... It depends! Size it correctly to meet the customer’s performance expectation
  Never create a pool or expand a pool with only a single SD. It will create a significant storage bottleneck regardless of the underlying disk configuration
  Max SDs per Stripe set is 32

## Slide 7: STORAGE POOL BEST PRACTICES CHUNK SIZE
Every stripeset is divided into chunks
A chunk is a region of disk space taken from a single stripeset
Whole chunks must be allocated (cannot allocate a fractional chunk)
It starts at the same location on all the SDs in the stripeset, and it draws the same amount of space from each SD
Prior to HNAS v11.2 the selection of the chunk size required some thought to balance granular capacity allocation and maximum scale
  Pre-HNAS 11.2, max chunks per Storage Pool was 16,384 and per File System 1,023
    Chunk size of 5GB restricted max File Systems size to ~5TB
    Chunk size of 256GB allows FS expansion to 256TB, but granularity of expansion is large

## Slide 8: STORAGE POOL BEST PRACTICES CHUNK SIZE (cont’d)
Post v11.2 max chunks per Storage Pool or File System is 60,000
  HNAS v11.2 storage pools created through the GUI do not allow you to set the chunk size – it will default to 1/3750 of the initial capacity of the span, ranging from 1GiB to 18GiB. CLI can be used to override
    18GB chunk size allows 1PB Storage Pool
  If starting with a very small amount of capacity, the default chunk size may not allow you to expand to 1PB
    Override by creating SPAN through CLI and setting chunk size manually
  HNAS v12.0 storage pools created through the GUI will select a mandatory default of 18GB chunk size
    CLI continues to use default (1/3750 of initial capacity) unless overridden manually.

## Slide 9: EXPANDING A SPAN
Expanding a span results in the creation of an additional stripeset
  A Span can be expanded up to 63 times
HNAS Dynamic Write Balancing (DWB) balances allocation of chunks to file systems across SDGs
  Still critical that SPANs expanded in a consistent fashion
Ensures that when additional disk is allocated to HNAS that all spindles can be utilized for write activity
  However in order to take advantage of those spindles, the pool and file systems must be expanded
HNAS Dynamic Read Balancing (DRB) is a utility that can be used to redistribute data evenly across SDGs
  DRB works best when existing span/file systems are close to max utilization
  See DWB Best Practices document for more info.
File System C
Stripe Set
SD
SD
SD
SD
SD
SD
SD
SD
Storage Pool
File System A
File System B
Stripe Set

## Slide 10: STORAGE POOL BEST PRACTICES EXPANDING A SPAN
Dynamic Write Balance (DWB) helps balance capacity (I/O) across stripe sets, however a performance bottleneck can still easily be created
Always expand stripe sets in a consistent manner to avoid creating a storage bottleneck.
  E.g. If the initial stripe set was created with 4 SDs, then expand by 4 SDs
This is especially important when existing span/file system are already heavily utilized (which is often when customers choose to expand them)

## Slide 11: STORAGE POOL BEST PRACTICES EXPANDING A SPAN (cont’d)
Dynamic Read Balance (DRB) should be used judiciously
  A span’s file Systems must only be expanded using chunks from the new stripeset in order to use DRB
    Pre HNAS v11.2 Can create a “dummy FS” to utilize all existing chunks and thereby avoid having to expand existing file systems
    HNAS v11.2 Can use the new option ‘filesystem-expand --on-stripeset’ to avoid creating a “dummy FS”
  DRB will cause snapshots to grow, as FS is rebalanced. It is therefore recommend that snapshots be deleted before running DRB
  DRB can help widen the storage bottleneck once it has completed (e.g. it can balance capacity across stripesets such that HNAS does not prefer all writes to one stripeset)

## Slide 12: FILE SYSTEMS
Filesystems are created on top of a span
Pre HNAS v11.2, a file system cannot grow larger than 1,023 chunks or 256TB (whichever comes first)
Post HNAS v11.2, a file system cannot grow larger than 60,000 chunks or 256TB (whichever comes first)
File systems are bound to an EVS (Enterprise Virtual Server)
You can pre-expand a filesystem or confine it to a maximum capacity and allow it to auto-expand as it fills, or let it auto-expand without a pre-defined confinement level (not typically recommended).
A file system can auto-expand as long as the span has space and the fs doesn't reach the max capacity or max chunk count.
A file system cannot be shrunk
Logical Storage Pool
Un-allocated Free Space
Virtual Volumes
Physical Disks
File Systems

## Slide 13: FILE SYSTEMS BEST PRACTICES AUTO-EXPANSION, BLOCK SIZE, UTILIZATION
Provides best efficiency with small files but should only be used with 10k/SSD drives
Is best suited to small block random I/O, 32kb FS to large block I/O
Should always be used with slower dense drives i.e. 7.2k SAS
Best suited to large block/sequential I/O
4 KB File Systems
32 KB File Systems
In many environments 32kb is a good fit, except when majority of files are small (capacity efficiency) or average I/O size is small (4-16kb) which could cause excessive RMW

## Slide 14: FILE SYSTEMS BEST PRACTICES AUTO-EXPANSION, BLOCK SIZE, UTILIZATION
In general it is advantageous to allow the file system to auto-expand as required for a few reasons
  It allows the chunk allocator to take advantage of new information -- for example, if one deletes file system A while file system B is still auto-expanding, the chunk allocator can back-fill previously used chunks by including them in file system B to balance load optimally across the stripesets.
  It allows capacity to be allocated on demand rather than “paying” up front for the capacity.
  File systems can't be shrunk, only expanded. Auto-expansion prevents possible over allocation of capacity that can’t easily be undone.
  Auto-expansion provides more optimal behavior in later code releases. In our 12.1 release which features HDP Integration, we strongly discourage large manual expansions since large expansion using HDP (1TB) could take multiple minutes to complete.
Notes: Auto-expansions come in two flavors: synchronous expansions, which occur when the FS hasn't room to satisfy a write request, and needs to expand before it can write the data; and asynchronous expansions, which occur when the FS notices (while taking a checkpoint, possibly) that free space is getting a bit low and adding a little more would help to keep performance up. A synchronous auto-expansion always takes as much space as it needs. That could be one chunk, but it could be more. Before 11.2, an asynchronous auto-expansion takes enough space to ensure that the fs is no more than 80% full, and it runs whenever used space exceeds 80%. From 11.2 onwards, an asynchronous auto-expansion takes enough space to ensure that the fs is no more than 80% full, but it doesn't run until the fs is 85% full; the effect is to perform fewer, larger expansions. From 12.1 onwards, and only on HDP pools, Span Manager limits the size of an asynchronous auto-expansion to roughly 32GiB. Synchronous expansions are not capped, and neither are expansions on plain (non-HDP) storage.

## Slide 15: FILE SYSTEMS BEST PRACTICES (cont’d) AUTO-EXPANSION, BLOCK SIZE, UTILIZATION
Avoid filling file system beyond specific capacity limits (80-90% max.)
  As file system fills the Superflush efficiency degrades
  Results in less sequential writes and more random writes
  FreeSpaceAllocator (FSA) spends more time searching for rather than allocating blocks
In general, avoid creating many small file systems (<1TB) and attempt to use larger file systems with multiple virtual volumes.
  At the time of writing this document, HNAS is limited to 128 file system in a single node or 125 in a cluster.
  Many file system that represent a small amount of data might may impact scalability (limited # of filesystems) or replication (# concurrent replication policies)
  Sometimes there are very good reasons to continue using multiple smaller file systems (snapshots & replication granularity)
File systems that are too large however could impact the scale of downtime in the event of catastrophic event
  Larger file systems take longer to fix should corruption/storage trauma occur
  Larger file systems take longer to backup/recover (NDMP backup)
In Summary, select the file system size appropriate to business requirements and HNAS scalability limits

## Slide 16: FILE SYSTEMS BEST PRACTICES (cont’d) Q DEPTH
Avoid multiple EVS sharing an HNAS storage pool
  HNAS Q-Depth per SD is 32. HNAS understands port Q-Depth limits of Hitachi Storage Arrays. SD Q-Depth is set at 32 regardless of underlying RG size or disk type within a specific array.
  If more than one EVS mounts file systems from the same pool across HNAS nodes, then SD queues are shared across two nodes reducing available Q-Depth per SD on each node
  If SDs that compose an HNAS storage pool are shared across two nodes (because the file systems on that pool are mounted by EVSs on each node), then Q-Depth per SD will be reduced to 16. This will likely incur performance penalties when under load.
EVS
EVS
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
FS
FS
FS
FS
SP
SP

## Slide 17: HNAS Storage – VIVOLS
HNAS delivers a method for partitioning the file systems called Virtual Volumes
Virtual volumes exist within file system subfolders
Capacity usage and file count limits (quotas) can be applied to both filesystems and virtual volumes
Virtual Volumes are logical containers, which can be grown and contracted with a simple size control implementation. Client machines see changes to the size of Virtual Volumes instantly
The sum of the space controlled by the Virtual Volumes may be greater than the size of the entire file system (over-subscription). Virtual volumes quotas do not track metadata overhead
Logical Storage Pool
Un-allocated Free Space
Virtual Volumes
Physical Disks
File Systems

## Slide 18: HDP SPECIFICS
Important Note: The information contained in the following HDP specific section is applicable to HNAS OS releases up to v12.0 – if you are using firmware levels beyond v12.0 please check with HNAS PM as these best practice guidelines are evolving and are subject to change

## Slide 19: Hitachi DYNAMIC PROVISIONING MANDATORY GUIDELINES FOR HDP USAGE WITH HNAS
HDP is supported with HNAS with two mandatory guidelines
  DP Pool must not be oversubscribed
    If dedicated pool set oversubscription to 95% or use Full Volume mode
  DP Volumes must never be re-sized
    HNAS volumes cannot be re-sized either online or offline
    To add storage to HNAS, create more SDs and add to/create new Storage pool

## Slide 20: HDP OVERPROVISIONING not supported with HNAS
HDP Pool
20TB
20TB RGs
8 TB
8 TB
8 TB
8 TB
8 TB
8 TB
8 TB
8 TB
DP Vols 64TB
8 TB
8 TB
8 TB
8 TB
8 TB
8 TB
8 TB
8 TB
HNAS Pool 64 TB
20
5
20
5
20
5
20
5
Allocated
Space
Total
Size
7
HNAS expands file system when usage reaches threshold. This allocates space from HNAS pool and succeeds
Later…
HNAS issues SCSI Write to new space.
X
DP Pool unable to allocate physical page
SCSI Write
SCSI Error
X
X
X
X
X
SCSI Write Fails
HNAS Pool Fails
HNAS File systems fail

## Slide 21: LUN PROVISIONING – BEST PRACTICES SYSTEM DRIVE GROUPS
HNAS v11.2 auto-groups DP-Volumes from the same HDP pool into a single parallel SDG
  Previous BP was to group each SD alone
  Changing requires un-mount of file systems
  Changing will only become necessary if a span must be expanded.
  SD’s grouped into a parallel SDG can only belong to a single tier.
HDP Pool should be dedicated to the Hitachi NAS cluster
  Sharing the pool with block devices is supported but not recommended
  On HUS1x0, AMS use Advanced Wide Striping Mode (AWS)
  On HUS-VM/VSP set SOM 917 to ON. This facilitates the balance of pages across Parity Groups rather than Pool Volumes
  On VSP/VSP G1000 set SOM 896 to ON; on HUS-VM set SOM 896 to OFF(default). This ensures that pages are formatted in the background rather than at allocation
SD
RG
RG
RG
RG
RG
SD
SD
SD
SD
SD
DPVOL
DPVOL
DPVOL
DPVOL
DPVOL
SDG
HDP POOL

## Slide 22: LUN PROVISIONING – BEST PRACTICES SYSTEM DRIVE GROUPS
HNAS v11.2 auto-groups DP-Volumes from the same HDP pool into a single parallel SDG
  Previous BP was to group each SD alone
  Changing requires un-mount of file systems
  Changing will only become necessary if a span must be expanded.
  SD’s grouped into a parallel SDG can only belong to a single tier.
HDP Pool should be dedicated to the Hitachi NAS cluster
  Sharing the pool with block devices is supported but not recommended
  On HUS1x0, AMS use Advanced Wide Striping Mode (AWS)
  On HUS-VM/VSP set SOM 917 to ON. This facilitates the balance of pages across Parity Groups rather than Pool Volumes
  On VSP/VSP G1000 set SOM 896 to ON; on HUS-VM set SOM 896 to OFF(default). This ensures that pages are formatted in the background rather than at allocation
SD
RG
RG
RG
RG
RG
SD
SD
SD
SD
SD
DPVOL
DPVOL
DPVOL
DPVOL
DPVOL
SDG
HDP POOL

## Slide 23: LUN Provisioning – BEST PRACTICES DP VOL – RG RATIO
The ratio of DP Volumes to physical RGs matters
  Undersubscribing will starve the storage
  Oversubscribing will overload the storage (HNAS QD per SD is still 32)
  General ratio is 1:1, but 2:1 could be used with larger 10k RGs and when using RAID10 with 10k drives
  When using HAF/SSD an 8:1 ratio provides best overall IOPS
RGs within the Pool should be consistent
DPVOL
DPVOL
DPVOL
DPVOL
RG
RG
RG
RG
HDP POOL
HNAS STORAGE POOL
Do not mix and match volumes in HNAS Pool
1:1 Ratio of DP Volumes to RGs
1 HNAS Storage Pool per DP Pool

## Slide 24: STORAGE POOL BEST PRACTICES – HDP STRIPESIZE and POOL EXPANSION
Maximum DP Volume size is 60TB, however on Enterprise platforms scalability could be reduced to 4TB for Max DP Volume size.
  TC, SI, HUR and UVM limit max volume size to 4TB as of the writing of this ppt. (Check with Enterprise Storage PM for latest information)
Guidelines for Stripe Sets and Storage Pool expansion still apply – even though HDP is performing wide-striping, Q-Depth across the stripe sets must still be sufficient and consistent
  Stripe Sets should still be expanded in a consistent fashion i.e. 2+2 or 4+4
  One should still allocate optimum number of DP Volumes per stripeset to provide sufficient Q-Depth to the underlying stripeset. 4 SDs per Stripeset is often used, but size appropriate to requirements.

## Slide 25: STORAGE POOL BEST PRACTICES – HDP (cont’d) STRIPESIZE and POOL EXPANSION
The need for DRB is minimized by HDP (due to block level restriping)
  For example a 4+4 Storage pool that is expanded by 4 SDs (4+4+4)
  If all chunks are already allocated, then HNAS writes will prefer the chunks allocated to the 3rd stripe set
  New Write I/O will be queued by HNAS to only 4 of the 12 SDs, however all data will be re-striped by HDP across all underlying spindles, thereby minimizing the need for DRB.
  DRB cannot be run against a file system when all SDs in a span reside in the same SDG (which is the recommended practice for HDP)

## Slide 26: HDP or NATIVE RG SHOULD I USE HDP OR NATIVE RG?
Generally speaking there should be little performance difference between HDP and non HDP configurations, provided Best Practices are followed
While it is possible to place multiple HNAS pools within a single HDP pool, this will not be a supported configuration in the future, therefore it is recommended that each HNAS span be mapped to it’s own HDP pool.

## Slide 27: FILE SYSTEMS BEST PRACTICES AUTO-EXPANSION, BLOCK SIZE, UTILIZATION
Non HDP configurations often utilize RAID5, especially when using 10k drives and small configurations; e.g. RAID5 4+1
  RAID5 is generally more I/O efficient than RAID6
HDP Configurations almost always use RAID6, per HDS Best Practices
  RAID6 provides a higher level of protection
RAID 5
RAID 6
In reality the choice of RAID5/RAID6 has nothing to do with HDP and has everything to do with managing risk, although many make that connection
RAID10 should also be considered for environments with heavy random write workloads, which can occur in HNAS environments experiencing poor superflush efficiency

## Slide 28: Questions and Discussion

## Slide 29: Thank You